## Slide 1: ECE 697CE: Foundations of Computer Engineering
Skill Building in C++ Programming Hints

## Slide 2: Objective
Write a detailed simulation program which simulates the MIPS architecture, cycle by cycle
Simulator should be
  Cycle-accurate with respect to register contents
  Display the contents of all the registers upon request
Please note that the hints presented in this chapter are mere suggestions. It is not mandatory to implement them as mentioned.

## Slide 3: Reading the Machine Code
Save the machine code as a text file, say code.txt
In the main program, read the text file and save it in the data structure used to implement Instruction memory.
  For example, Instruction memory could be implemented using a character array:
    char IMem[2048]
  Hint: You may use the stringstream functions in C++ to convert the string in the text file to numbers

## Slide 4: Main Components
The main components
  Functional Units : IF , ID , EX , MEM , WB
  Registers in between the functional units : IF_ID, ID_EX, EX_MEM, MEM_WB
  32 Registers
  PC
  Memories : Instruction and Data

## Slide 5: Implementing the Functional Unit
Hint: One may use functions to implement functional units: IF(), ID(), EX() , MEM(), WB()
In MIPS, IF stage takes as input the contents of IF_ID register and stores the result in the ID_EX register
Similarly ID stage takes as input the contents of ID_EX register and stores the result in the EX_MEM register and so on.
Note that the functional units can take other registers as inputs too.
  For example, When a branch is detected and the IF stage has to fetch an instruction located at the branch target address, it requires the contents of EX_MEM register.

## Slide 6: IF Stage
IF stage
  IF/ID.IR <- Mem[PC];
    If ((EX/MEM.opcode ==branch) & EX/MEM.cond )
    IF/ID.NPC, PC <- {EX/MEM.ALUOutput}
    else
    IF/ID.NPC, PC <- {PC+4})
Adapted from ECE 568 Computer Architecture, Israel Koren

## Slide 7: ID Stage
ID stage
  ID/EX.A <- Regs[IF/ID.IR[rs]];
  ID/EX.A <- Regs[IF/ID.IR[rt]];
  ID/EX.NPC <- IF/ID.NPC;
  ID/EX.IR <- IF/ID.IR;
  ID/EX.Imm <- sign-extend(IF/ID.IR[immediate field]);
Adapted from ECE 568 Computer Architecture, Israel Koren

## Slide 8: When Does MIPS Sign Extend?
When value is sign extended , copy upper bit to full value:
Examples of sign extending 8 bits to 16 bits:
  00001010 -> 00000000 00001010
  11111101 -> 11111111 11111101
Arithmetic instructions sign extend immediates even for the unsigned versions of the instructions
Logical instructions do not sign extend

## Slide 9: EX Stage
ALU instruction
  EX/MEM.IR <- ID/EX.IR;
  EX/MEM.ALUOutput <- ID/EX.A func ID/EX.B;
  or
  EX/MEM.ALUOutput <- ID/EX.A op ID/EX.Imm;
Load or store instruction
  EX/MEM.IR <- ID/EX.IR;
  EX/MEM.ALUOutput <- ID/EX.A + ID/EX.Imm;
  EX/MEM.B <-ID/EX.B; (for store)
Branch instruction
  EX/MEM.ALUOutput <-ID/EX.NPC + (ID/EX.Imm <<2);
  EX/MEM.cond <- (ID/EX.A == 0);

## Slide 10: MEM Stage
ALU instruction
  MEM/WB.IR <- EX/MEM.IR;
  MEM/WB.ALUOutput <- EX/MEM.ALUOutput;
Load or store instruction
  MEM/WB.IR <- EX/MEM.IR;
  MEM/WB.LMD <- Mem[EX/MEM.ALUOutput];
  or
  Mem[EX/MEM.ALUOutput] <- EX/MEM.B;

## Slide 11: WB Stage
ALU instruction
Regs[MEM/WB.IR[rd]]<-MEM/WB.ALUOutput;
  or
  Regs[MEM/WB.IR[rt]] <- MEM/WB.ALUOutput;
Load or store instruction
For load only:
Regs[MEM/WB.IR[rt]] <- MEM/WB.LMD;

## Slide 12: Implementing the Pipeline Registers
IF/ID, ID/EX, EX/MEM,MEM/WB :- registers of the 5 stage pipeline
Latches in each register
  IF/ID: IR, NPC
  ID/EX: IR, NPC, A, B , Imm
  EX/MEM: IR, B, ALUOutput , cond
  MEM/WB: IR, ALUOutput, LMD
Hints:
  Can be implemented using class
  Class contains IR ,A ,B ,Imm and other latches as private members.
  Can use get() and set() functions to access the private members of the class
  Objects of the class could be IF_ID, ID_EX,EX_MEM,MEM_WB

## Slide 13: Class to Implement Latch
class latchReg
{
};
private:
  unsigned long int IR;
  unsigned long int NPC;
  unsigned long int A;
  unsigned long int B;
  unsigned long int Imm;
  unsigned long int ALUOutput;
  unsigned long int cond;
  unsigned long int LMD;
Latches as private members
public:
  static unsigned long int R[32];
  static unsigned long int PC;
32 Registers and PC as static members
latchReg IF_ID;
latchReg ID_EX;
latchReg EX_MEM;
latchReg MEM_WB;

## Slide 14: Implementing Memories
Use char arrays of size 2k to implement Data and instruction memory
            char IMem[2048];
            char DMem[2048];
Hint: To access a word from DMem (if address is given as the index)
          data=(DMem[address]<<24)|
          (0x00FF0000&(DMem[address+1]<<16))|
          (0x0000FF00&(DMem[address+2]<<8))|
          (0x000000FF&DMem[address+3]);
Hint: Access an instruction from IMem in a similar manner

## Slide 15: Registers and PC
32 registers
R0 hardwired to 0
Hint: You may use array of 32 long unsigned int to store the registers and a long unsigned int to store PC
Name | Registers | Usage
$zero | 0 | The constant value 0
$at | 1 | Reserved for assembler
$v0-$v1 | 2-3 | Values for results and expression evaluation
$a0-$a3 | 4-7 | Arguments
$t0-$t7 | 8-15 | Temporary registers
$s0-$s7 | 16-23 | Saved registers
$t8-$t9 | 24-25 | More temporary registers
$k0-$k1 | 26-27 | Reserved for operating system kernel
$gp | 28 | global pointer
$sp | 29 | Stack pointer
$fp | 30 | Frame pointer
$ra | 31 | Return address

## Slide 16: Implementing Parallel Execution in a Sequential Machine
2 ways to implement the parallel execution of all the functional units using a sequential machine
  Call IF , ID , EX, MEM , WB in the order mentioned
      IF operates on 5th instruction
      ID operates on 4th instruction
      EX operates on 3rd instruction and so on
    Execution of IF stage before ID stage will cause the values of IF_ID register to be overwritten.
    Instead of operating on the 4th instruction, ID stage would operate on the 5th instruction
    Prevent this by using temporary registers
  Call WB, MEM, EX, ID, IF in the order mentioned
    Slightly complicated but prevents the need for temporary registers
      IF operates on the 5th instruction
      ID operates on the 4th instruction and so on

## Slide 17: Other Remarks
No interrupts
Does not support out-of-order execution
Only one instruction can occupy a given pipeline stage at any time
  This may cause other instructions to be stalled
Must take care of structural, data and control hazards
Does not support data forwarding
Assume that register writes are completed in the first half of a clock cycle
Register reads are carried out in the second half

## Slide 18: Dealing With Branches / Control Hazards
When the branch is detected (in the ID stage)
It should tell the IF stage to stop fetching
It should flush the IF-ID register (i.e., insert NOPs)
When the branch is resolved (in the EX stage),
Resume fetch of instructions based on the branch outcome

## Slide 19: Structural Hazard
Structural hazard occurs
  Execution unit is busy
  Data memory is busy ( being accessed by other instruction)
Structural hazard : If EX unit is busy due to instruction i,
  assume EX/MEM register cannot be written till i completes execution
  assume ID/EX register cannot be overwritten by instruction i+1

## Slide 20: Data Hazard
Source registers in the ID stage are compared with the destination registers in EX/MEM and MEM/WB stage
Comparison only if source registers are Read Enabled and destination register is Write enabled

## Slide 21: Outputs of the Simulator
The output of the simulator will be the following statistics:
  Utilization of each stage: Utilization is the fraction of cycles for which the stage is doing useful work. Just waiting for a structural, control, or data hazard to clear in front of it does not constitute useful work.
  Total time (in CPU cycles) taken to execute the MIPS program on the simulated machine. (This is NOT the time taken to execute the simulation; it is the time taken by the machine being simulated.)